Reason for note:

Due to a THD+N error which only occurs  when analog input is selected while a signal is feeded to AES or S/P-Dif, it is necessary to implement a 56R resistor in series with 64FS clock to the AD converter.

Actions:

The Resistor should be mounted on the lower side of the P13001-4 mainboard just under the DARC3 chip. Scrape away so the track is intermittent and make the to ends of the track blank so you can solder the resistor on to it  Please see picture below for the exact location.

IMPORTANT:

This replacement should only be carried out by skilled technicians.